## Slide 1: DSD Presentation RISCV-G3
B07901021 潘世軒
B07901036 陳俊廷
B07901137 吳陽禾

## Slide 2: Outline
Baseline
Extension
  Branch prediction
  Compression
  L2 cache

## Slide 3: Outline
Baseline
Extension
  Branch prediction
  Compression
  L2 cache

## Slide 4: Optimization: move logic before ff to save area
Before: FF 65 bits
Before: FF 32 bits
And make sure the critical path won’t be longer !
1
32
32
32

## Slide 5: Optimization: Stall for specific branch, jalr
Main purpose: shorten the critical path
We do the same thing for jalr case
But jalr case didn’t appear in I_mem_hasHazard

## Slide 6
addi x11 x11 0x004
bne x11 x12 Inloop
Before stalling

## Slide 7
addi…
nop
After stalling
bne x11 x12 Inloop

## Slide 8: Optimization: flipflopped mem_ready
Add a flipflop for mem_ready
Make sure we have enough time to do the following things
Decoder, multiplexer…
No setup time violation !

## Slide 9: Optimization: direct-mapped Icache
Instructions are executed sequentially (sometimes loop)
Using direct-mapped Icache can reduce the cost of decoder, mul…
Also, it can shorten the “hit access time” of Icache
Direct-mapped
2-way associative
Notes: 這頁可以不要講

## Slide 10: Our AT value:
sdc cycle: 2.55
Total time: 4945.26 (tb =2.41)
Area: 295357.8

## Slide 11: Outline
Baseline
Extension
  Branch prediction
  Compression
  L2 cache

## Slide 12: Block diagram
B: Jal “beq always branch” move it to IF stage along with beq, bne
A: BPU for beq and bne predict for taken or not taken
FSM
No need to stall for the following case: (because of the change of critical path)
A
B

## Slide 13: Finite State Machine
Notes: 這頁可以不要講

## Slide 14: Experiment1
Change runtimes of part C (always branch) (a10b10) -> Good Prediction
Change runtimes of part A (never branch) (b10c10) -> Good Prediction
Notes: 這頁可以不要講

## Slide 15: Experiment1
Change runtimes of part B (interleaved) (a10c10) -> Cannot handle it
Worst case: 100% failed
Best case: 50% failed

## Slide 16: Experiment2
Use two circuits to execute I_mem_hasHazard. I cancel the stalled cycle for above case. So the only difference is the BPU. Baseline always fetch PC+4 first -> PREDICT NEVER TAKEN
Cumulative cycles
Fibonacci: always taken
Bubble sort:
  Swap in inner loop: Random (never taken)
  Inner loop: always taken
  Outer loop: always taken
Bubble sort output: always taken
actually
Notes: 這頁可以不要講
提swap那裏會造成交錯就好

## Slide 17: Summary
Characteristics of 2-bit predictor
  1. Can deal with single loop (always taken or never taken)
  2. Can deal with one “if” in single loop (Look before you leap!)
  EX: swap in inner loop
  3. Cannot deal with interleaved pattern

## Slide 18: Experiment3
Branch prediction unit: can do prediction but at the cost of area and the increase in critical path
To see how this trade-off affect the performance, I run I_mem_hasHazard_modified for BPU and baseline after synthesis

## Slide 19: Experiment3

## Slide 20: Experiment3
Due to the gap of cycle, Baseline still win in time.
But actually, CPU with such high frequency will consume much more power.
So I think using Branch prediction unit in CPU is a good choice and it can decrease the run time and run cycle.

## Slide 21: Other architecture of BPU
Branch prediction buffer (cache)
Consider the miss for 1-bit predictor (leave loop and enter loop -> wrong) I put 2-bit predictor in FSM for each address
Fully-associative (check all address)
Replacement policy: bit-pseudo-LRU
  When the addr used, assert its status (0->1)
  When all status asserted, clear (all to 0)
  When addr miss, choose block with status to be replaced

## Slide 22: BPB
Flow diagram of IF stage ->
We can find that the performance of BPB is further improved

## Slide 23: Outline
Baseline
Extension
  Branch prediction
  Compression
  L2 cache

## Slide 24: Target
Decompress
PC control
I_CACHE alignment

## Slide 25: Instruction Type

## Slide 26: Decompress + PC Control

## Slide 27: ICACHE
If the offset is 7(ex: 0x4E), and the next instruction is 32 bits, then cross_over = 1, we need to read the next block(0x50).

## Slide 28: Performance
Sdc Cycle(ns) | 3
Design Area(μm^2) | 18338.709635
Decompression Execution Cycle | 520.5
Compression Execution Cycle | 431.5
Decompression ICACHE stall | 14
Compression ICACHE stall | 8

## Slide 29: Outline
Baseline
Extension
  Branch prediction
  Compression
  L2 cache

## Slide 30: Why L2 Cache ?
L1 Cache miss penalty too big
(6% in baseline tb, 7.5% in L2 tb)
Definitely be larger in reality

## Slide 31: Two types of L2 Cache
Split Cache Unified Cache
Can reduce write logic in L2 I-Cache
Shorter tag(address) matching time
Simpler logic design
Bigger bandwidth
Lower miss rate due to more blocks
(Unified Cache is more common in recent years.)

## Slide 32: Split Cache
After implementation, we found that L2 D-Cache improve 14% performance

## Slide 33: Split Cache
After implementation, we found that L2 D-Cache improve 14% performance
Due to L2 I-Cache’s 80% miss rate
BUT
L2 I-Cache won’t do any better on L2’s tb

## Slide 34: Split Cache
After implementation, we found that L2 D-Cache improve 14% performance
Due to L2 I-Cache’s 80% miss rate
(tb too simple)
BUT
L2 I-Cache won’t do any better on L2’s tb
miss rate: I-Cache/ D-Cache

## Slide 35: Split Cache
Therefore, we add some nop in swap loop(bubblesort) to make instruction more complicated.
32 nop
(because L1 cache can store 32 instructions)

## Slide 36: Split Cache
Results for modified L2 Cache tb
33% improved
L2 I-Cache finally do something!

## Slide 37: Unified Cache
Larger area
(Can’t reduce I-Cache’s write logic)
4K D-Cache = 30W
4K I-Cache = 22W
8W reduced
Proof I

## Slide 38: Unified Cache
Larger area
(Can’t reduce I-Cache’s write logic)
Proof II
Big difference in Combinational part
Non-combinational almost the same
Unified
Split

## Slide 39: Unified Cache
Again, compare to size of L2 Cache, tb is too easy…
Can’t observe the benefit of using unified cache
miss rate: I-Cache/ D-Cache (weighted average)

## Slide 40: Unified Cache
Use total 32 blocks instead of 64 blocks
(L1 size x2)
miss rate: I-Cache/ D-Cache (weighted average)
Unified performs a lot better